Jim Scarsella

847 Washington Rd.

Grosse Pointe, Michigan 48230

313-220-5077

www.jimscarsella.com

email:woodart@jimscarsella.com

Carving Supply Sources

MDI Woodcarvers Supply		Stump Cutters, Mini Stump Cutter Sets,

800-866-5728				Small Tapered Mini Paper Cartridge Rolls, www.mdiwoodcarvers.com		Pfingst Micro Sander, Kutzall Bits

Wood Carvers Supply		Mastercarver Micro-Pro (Micro Motors)

800-284-6229

www.woodcarverssupply.com

Rio Grande				Lynx Round Burs (all sizes)

Tools & Equipment   			3M Radial Bristle Discs

800-545-6566

www.riogrande.com

Craft Supplies USA			NSK Presto High Speed Carver

800-551-8876		 		Carbide Carving Bits

www.woodturnerscatalog.com

Christian J. Hummul Company	3M Radial Bristle Discs, Stump Cutters

800-762-0235

www.hummul.com

Packard Woodworks Inc. 		Mastercarver Micro-Pro (Micro Motors)

800-683-8876				Woodburning Supplies

www.packardwoodworks.com

References:

Woodcarving Magazine, “Choosing Power Carving Bits”, Fall 2009 Issue #48, Editors

http://www.woodcarvingillustrated.com/tools-and-tips/choosing-power-carving-bits.html

Wood Magazine, “Power-Carving Bits”

http://www.woodmagazine.com/woodworking-plans/routing/power-carving-bits/

Topics

Preferred Wood

I prefer the “soft hardwoods”. They are strong and hold fine detail yet fairly easy to power carve.

- Cherry

- Walnut

- Soft Maple (Red Maple, Silver Maple)

- Sycamore

- Box Elder

Turning for Carving: Things to Consider

- Shape

- Areas of extra material?

- How to start and terminate carving?

- Overall Wall Thickness (consider depth of relief)

- Grain orientation. Depending on carving pattern can affect strength of fine detail.

Dust Collection

- Dust Bee Gone Mask (woven polyester filter fabric, washable & lasts indefinitely)

Loops

Positioning Work & Comfort

Pillows, Beanbags, Old Towels

Patterns: Vyco Board (Pattern Material), cuts easily with Exacto knife, molds easily, a bit expensive. Available at many sources on-line.

NSK Presto High Speed Carver

- Air turbine operated

- Compact- hand piece measures 5/8" diameter by 4 1/4" long

- 1.5 cfm required- works on most compressors 3/4 h.p. or higher

- 1/6” Shank Bits

- 320,000 rpm operating speed @ 35 psi, 400,000 rpm @ 40 psi

- Oil-less operation

- Quick Changing Coupler

- Short Carbide Bits Rated for High Speed

- Blows away debris making work easier to see

- Clean with mild steel

- Preferred Bits:

  - Round Cutters

  - Round End Tapered Fissure Cutter

Power Carving Units

Micro Motors - Mastercarver Micropro

- From under $100 - $1,500

- Compact- hand

- 3/32” or 1/8” Shank Bits

- 35,000 to 50,000 rpm operating speed

- Quick Changing Coupler

- Huge selection of bits

Shaft Driven Tools

- Fordom

- Appprox 15,000 rpm

- Require tools to change bits

- Powerful, high torque Machines

- Take multiple size bits (3/32” to ¼” shafts)

- Vibration!!

- Loud

Stump Cutters: Useful Shapes

- Can alter shape by grinding

- Round

- Flame

- Bud

- Rounded Cylinder Mini Stump Cutter Set (MDI 21-Set 35)

- Pointed Cone Mini Stump Cutter Set (MDI 21-Set 39)

- Clean by running in a brass brush

Sanding Tips

- Pfingst Micro Sander

- 3M Radial Bristle Discs (Stack 5-6)

- Small Tapered Mini Paper Cartridge Rolls

- Ruby, and Ceramic Bits

- Diamond Bits (inexpensive, come in sets with multiple shapes)

- 3M Foam Tape (2 Sided)

- Round Punches (Scrapbooking)

- Emory Boards

Woodburning Tips

- Units

  - Variable Heat Control

  - 100 Watts or higher

  - Colwood- Olympiad

  - Burnmaster- Hawk or Eagle

  - Detail Master-Sabre IV or Excalibur

- Writing Tips

  - Fixed Tips

  - Flexible Cords

  - Skew Tip (Keep Sharp)

  - Ball Tips

- Clean with Brass Brush

- Toothbrush

- Small fan to clear smoke- not on tip

India Ink (Speedball): Deeper black

Tandy Dye: USMC Black